## Slide 1: Single Camera Calibration using Partially Visible Calibration Objects Based on Random Dots Marker Tracking Algorithm
*Yuji Oyamada1,2, Pascal Fallavollita2, and Nassir Navab2
1. Keio University, Japan 2. Chair for Computer Aided Medical Procedure (CAMP), Technische Universität München, Germany
*contact: oyamada@in.tum.de
http://campar.in.tum.de/Main/YujiOyamada

## Slide 2: Overview of this work
Use a marker tracking algorithm for a single camera calibration.
Input
Marker tracking result
Notes: Practical application that is based on state-of-the-art marker tracking algorithm.
Specifically, random dots tracking algorithm for solving points correspondence issue of camera calibration

## Slide 3: Overview of this work
Use a marker tracking algorithm for a single camera calibration.
Calibration result
Notes: Practical application that is based on state-of-the-art marker tracking algorithm.
Specifically, random dots tracking algorithm for solving points correspondence issue of camera calibration

## Slide 4
Introduction

## Slide 5: Camera calibration
Goal: finds a relation between
  3D real world and 2D camera image.
  different cameras.
Necessary step for vision based applications:
  3d reconstruction,
  augmented reality.
projection
projection
projection
Notes: single calib: 3d - 2d
multiple calib: camera - camera
This work focuses on the top one.

## Slide 6: Calibration procedure
Two main steps:
  finds correspondence between real world and camera images.
  computes parameters describing the relation.
Intrinsic parameters:
Lens distortion parameters:
Extrinsic parameters:
Notes: basic strategy takes two steps.
1. points correspondence: detection & identification
several ways for correspondences: manual click,
2. parameter estimation:
research issue on this step is what kind of constraints we use: camera geometry, linear algebra, optimization...
this paper focuses on the first step

## Slide 7: Well-known & well-used method
Zhang's method [26]:
  uses several images of a set of known control points on a planar objects.
  step-by-step parameters estimation.
MatLab Camera Calibration Toolbox [3]
[26] Z. Zhang, ICCV, 1999
[3] J. Y. Bouget, MatLab Camera Calibration Toolbox, 2008
Notes: Zhang's planar based calibration

## Slide 8: For accurate calibration...
Calibration object should be 3d:
  Fill entire view volume
  Different poses >> same pose
  Different depths >> same pose
Notes: Our dilemma occurs from assumption on control points identification

## Slide 9: Our dilemma
Strong assumption: entire object must be visible.
For localization: hesitates to go closer to image border.
For accuracy: better to go as close to image border as possible.
Notes: Our dilemma occurs from assumption on control points identification

## Slide 10: Literature: points correspondence
 | Circle/rings grid [4] | AR Tag [7] | Natural image [19]
Occlusion | X | O | O
Defocus | O | X | O
Perspective distortion | △ | O | △
[4] Datta, ICCV workshop, 2009
[7] Fiala, MVA, 2008
[19] Pilet, ISMAR, 2006
Notes: before going to the description of the proposed method,
let me mention the literature here

## Slide 11: Motivation
Remove the assumption = Handle partial occlusion.
More accurate estimation by filling view volume.
Less frustration during image acquisition.
Notes: Our dilemma occurs from assumption on control points identification

## Slide 12: Motivation
Especially, useful for multiple cameras calibration (though this work focuses on single camera calibration...)
Hundreds of cameras
The Stanford Multi-Camera Array
Distributed cameras Eyevision, CMU
Different types of cameras HMD based AR, TUM

## Slide 13
The proposed method

## Slide 14: Our idea
Idea: Uses state-of-the-art marker tracking algorithm.
  Automatic detection and localization even with partial occlusion. = Can put calibration object closer to image border.
so that
  More accurate estimation on lens distortion parameters.
  Flexible calibrations for vision based systems.
Notes: our idea for solving this dilemma

## Slide 15: The proposed method
Points correspondence: applies tracking algorithm on the images.
Parameter estimation: optimizes using the points correspondence.
RANdom DOts Marker

## Slide 16: Method 1/2: overview
Applies RANDOM tracking algorithm [22] on the images.
  Simple circle detection.
  Fast matching using LLAH.
Circle detection
Input
Points matching
[22] Uchiyama, IEEE VR, 2011

## Slide 17: Method 1/2: tracking algorithm
Tracking algorithm [22] invariant to scale & rotation.
  Use distribution of control points.
  For a point of interest, set of ratio of two triangles consists of its neighboring points.
[22] Uchiyama, IEEE VR, 2011

## Slide 18: Method 2/2: parameter estimation
Based on Zhang's method [26].
  Non-linear optimization on reprojection error of control points.
  Consider the visibility of control points.
(11)
[26] Z. Zhang, ICCV, 1999

## Slide 19
Experimental results

## Slide 20: Experiments
Simulation experiments:
  RANDOM with 200 control points.
  Chessboard with 40 control points
Real world experiment:
  RANDOM with 200 control points.
200 points on RANDOM
40 points on chessboard

## Slide 21: Simulation experiment 1/2
Q: More accurate result with marker located around image border?
Comparison:
  10 images from (a).
  10 images from (a) + 1-10 images from (b).
(a) Entire RANDOM
(b) Partial RANDOM

## Slide 22: Simulation experiment 1/2: result
Error: mean value
Error
Error
0
10
0
10

## Slide 23: Simulation experiment 1/2: discussion
Two disadvantages:
  Center of circle is not perspective invariant.
  Inaccurate detection due to poor circle detection algorithm.
: detected points : reprojected points
2 pixels difference!

## Slide 24: Simulation experiment 2/2
Q: Is the proposed method better than chessboard one?
Comparison:
  10 images from (a).
  10 images from (a) + 10 images from (b).
  10 images from (c).
  20 images from (c).
(a) Entirely visible RANDOM
(b) Partially visible RANOM
(c) Entirely sible chessboard

## Slide 25: Simulation experiment 2/2: result
Our method results less reprojection error.
Notes: 2 remarks:
less mean error = more accurate
less standard deviation = more stable
same number of images, chessboard should be better (1) control points on chessboard are robust against perspective distortion while ones on RANDOM are against only scale and rotation
(2) because off sub-pixel accuracy control points detection
maybe RANDOM has much more control points

## Slide 26: Simulation experiment 2/2: result
It's strange that case 1 outperforms case 3 because
  control points on a chessboard is perspective invariant,
  control points on RANDOM is
    scale & rotation invariant,
    center of circle is not perspective invariant.
The result may be due to number of control points.
  200 control points on RANDOM
  40 control points on chessboard
Will perform more fair comparison...

## Slide 27: Real world experiments 1/2
Single camera calibration: Sony Nex-5.
  Resolution: 1920x1080
  Number of images: 100
  Number of control points on RANDOM: 200

## Slide 28: Real world experiments 1/2: result

## Slide 29: Real world experiments 1/2: result
Reprojection error: 0.16 ± 0.15 pixel
Maximum error: 1.30 pixels

## Slide 30: Real world experiments 2/2
Multiple cameras calibration (3 cameras attached on an HMD):
  1 IR camera
  2 color cameras

## Slide 31: Real world experiments 2/2: result
Notes: you can see top IR camera sees upper while bottom color cameras see straight.
calibration images are concentrated on bottom
= less overlap between top and bottom

## Slide 32
Conclusion
+
future works

## Slide 33: Conclusion
Used marker tracking algorithm
To solve points correspondence problem
For more accurate & friendly camera calibration.
Advantage:
  More accurate & stable calibration result.
  Many potential extensions.
Limitation:
  The tracking algorithm is only scale & rotation invariant. = heavy rotation along x/y axis is not supported.
  Center of circle is not perspective invariant.

## Slide 34: Potential extension
Multiple cameras calibration.
Multiple markers for calibration [A1].
[A1] GML Camera Calibration Toolbox, 2005

## Slide 35: Potential applications
Different types of cameras: combination of color & IR markers
Projector-camera: one printed and one projected markers.
Distributed cameras: multiple markers.
Pro-Cam pair
P
C
IR & color cameras
IR
C
Distributed cameras

## Slide 36: Future works: tracking for points correspondence
Use perspective invariant metric for points correspondence.
  line segments tracking [A2].
Center of circle is not perspective invariant.
  Use perspective invariant mark [A3].
Line segments tracking_
for SLAM [A2]
Perspective invariant mark
[A3]
[A2] Hirose, BMVC, 2012
[A3] Beeler, Tech. rep. ETHZ, 2010

## Slide 37: Future works: tracking for calibration constraints
Uses rigidity of cameras for non-overlapping cameras calibration.
  Tracking for knowing each camera motion,
  Then align the unsynchronized cameras using their rigidity [A4].
Selects good calibration images from long video sequences.
  Somehow evaluate calibration images
  To reduce unnecessary huge amount of images from video sequences.
[A4] Irani, IJCV, 2002

## Slide 38: Code available
Entire package containing tracking and calibration by me.
  will publish as an open source
  current version: C++ + MatLab
  future version: C++
  If you want to use it, please contact me!
Original RANDOM tracking algorithm by Hideaki Uchiyama [22].
  open source
  C++
User friendly calibration code on github by Alexandru Duliu.
  open source
  C++

## Slide 39: Thanks for your attention...
I'm looking for a job opportunity.
present-03.2013: postdoc @ Keio Univ. & visiting postdoc @ TUM
03.2012-??: not decided yet...
My research interests
  camera tracking for practical application,
  image restoration
    deblurring
    focus control
  3d modeling
    3d reconstruction using depth camera
    photometric stereo
  AR visualization to improve perception

## Slide 40: Acknowledgments
This work was partially supported by the Strategic Young Researcher Overseas Visits Program for Accelerating Brain Circulation of Japan Society for the Promotion of Science, G2308